FOR IMMEDIATE RELEASE

AS Project Co. First to Install Focusrite RedNet in Japan

RedNet user base continues to expand globally

Los Angeles, CA, July 16, 2013 – RedNet is Focusrite's flagship modular high-quality audio networking system based on Dante®'s powerful digital audio network. AS Project Co. Ltd., located in Shinjuku, Tokyo, recently became the first users of RedNet in Japan.

AS Project Co. specializes in live and event sound and has been using the Yamaha CL live console series in conjunction with Pro Tools HD. As existing Yamaha CL series users, AS Project Co. decided to take advantage of the fact that the console has built-in Dante functionality by choosing RedNet 5. Two RedNet 5 units are connected to Pro Tools HD and to the Dante network, allowing 64 channels of high-quality, uncompressed digital audio to pass between the console and the recording system.

Sound engineer Masahiro Fukuhara spoke about his implementation and initial thoughts of RedNet: "RedNet 5 is recognized immediately as two 192 Digital I/O™ units from the Pro Tools® side, and therefore the routing is very straightforward. RedNet Control and Dante Controller are installed in the MacBook Pro with Nuendo Live. Pro Tools HD is installed on the main Mac Pro machine and Nuendo Live works as a backup for recording. Within the Dante network, digital audio signals for recording are connected through a Gigabit Luminex GigaSwitch 8 Ethernet switch. Long-distance cabling requirements are taken care of by high-quality Cat5e cable. The master clock from the system is taken from a black burst generator converted to word clock by a SYNC I/O™ into the Yamaha CL5, which is then the master clock for the Dante network. RedNet 5 provides the loop sync for an additional 192 I/O™. I've had experience with Dante, but installing RedNet 5 was easy – just connect and power-on. We've already used it for some live recordings, and it's worked well every time."

192 I/O, SYNC I/O and Pro Tools HD are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries.

Photo File: RedNet5.JPG

For further information, head to www.focusrite.com or contact:

USA: Hannah Bliss +1 (310) 322 5500 // Hannah.Bliss@focusrite.com

Robert Clyne  +1 (615) 662-1616 // robert@clynemedia.com

About Focusrite

The Focusrite brand was established in 1985 and the founding principles of the company were to develop products that sounded more musical, in addition to just measuring well – today, we still carry these founding principles forward in our class-leading and award-winning designs. We measure our success by the success of you, our clients, and you will find Focusrite product prominent in professional and project studios throughout the world. Based just outside of London, we work with the best design talent throughout the world to bring you the tools to enhance the way you work. Our product is made with pride and principle in a highly automated ISO 9002 factory with significant level of test by engineers who themselves are musicians and understand the part our product plays in your process.