PRESS RELEASE

Media Contact: Robert Clyne

Clyne Media, Inc.

Robert@clynemedia.com

Tel: (615) 662-1616

Fax: (615) 662-1636

FOR IMMEDIATE RELEASE

Lowell Introduces Updated LH Series Horn

— New model offers optional adaptors to meet IP66 rating for water- and dust-resistance —

INFOCOMM, LAS VEGAS, NV, June 13, 2012 — Lowell Manufacturing Company (booth C9723), a U.S. manufacturer of professional A/V Products currently celebrating its 65th anniversary, has introduced an updated version of its LH Series double re-entrant horn that features an improved frequency response and is IP66 rated for water- and dust-resistant operation when used in conjunction with the optional adaptors. Available in a 15W or 30W model, the LH Series is offered with a beige finish that allows it to blend into environments such as schools, recreational facilities, warehouses, distribution centers, parking facilities and commercial buildings.

Lowell’s LH horns incorporate a high efficiency compression driver for high intelligibility and are designed for clear voice paging and tone signaling applications in a variety of indoor and outdoor applications. Both models offer easy, two-wire connection using rear screw terminals and include a built-in, screwdriver-adjustable transformer for integration into 25V, 70V or 100V applications. The supplied swivel mounting bracket permits precise orientation.

Horn Model LH-15TA (15W) operates within a frequency range of 537 Hz – 4.5 kHz (±6 dB) with a sensitivity of 112.2 dB log average (1W/1M) 124.0 dB maximum SPL.  Model LH-30TA (30W) operates within a frequency range of 411 Hz – 4.0 kHz (±6 dB) with a sensitivity of 118.1 dB log average (1W/1M) 138.8 dB maximum SPL. Calculations are based on power rating and measured sensitivity.

Optional adaptor Models LHA-15G and LHA-30G feature a waterproof strain relief grommet for cable input. Models LHA-15C and LHA-30C feature a threaded conduit fitting.

For more information, please visit www.lowellmfg.com or e-mail Lowell at sales@lowellmfg.com.

###

Photo File: LH-15TA.JPG

About Lowell Manufacturing

From its headquarters located just south of St. Louis, Missouri, Lowell engineers and manufactures rack, power and audio products for the professional AV, custom installation and broadcast markets. Company history dates back to 1947 when founder Ben Lowell pioneered the idea of using a loudspeaker ceiling baffle to balance sound distribution throughout large spaces. Today, the next generation of the Lowell family works with a highly experienced sales and engineering team to convey that same spirit of innovation in developing high-performance, value-based products for the sound and communications industry.

Lowell contact info:

Kathleen C. Lane

Marketing Communications Manager

klane@lowellmfg.com

Tel: (800) 325-9660

Lowell Manufacturing Company is exhibiting at booth C9723 at InfoComm 2012 in Las Vegas, Nevada.