PRESS RELEASE

Media Contact: Robert Clyne

Clyne Media, Inc.

Robert@clynemedia.com

Tel: (615) 662-1616

Fax: (615) 662-1636

FOR IMMEDIATE RELEASE

# Lowell Introduces “Universal” Fan Panels

— Rackmount fan panels with universal input voltage and three adaptor plugs,

plus optional thermostat probe —

INFOCOMM, LAS VEGAS, NV, June 13, 2012 — Lowell Manufacturing Company (booth C9723), a U.S. manufacturer of professional A/V Products currently celebrating its 65th anniversary, will introduce its new line of fan panels at InfoComm 2012. The FDC series of 19” rackmount panels offers universal input voltage (100VAC–240VAC) and includes a UL Listed power supply with three plug adaptors to accommodate outlet requirements in North America (NEMA 1-15), central Europe (Schuko CEE 7/16) and the U.K. (BS1363).

Panels are available in 2RU or 3RU with different size fans. Model FDC4-2 features four fans with 80mm diameter each (3.15-in.), providing total airflow of 104cfm (29db). Model FDC3-3 includes three fans with 120mm diameter each (4.72-in.) for total airflow of 220cfm (38dB).

A big plus in energy-savings is the optional vari-speed thermostat probe, which automatically activates fans when ambient temperature hits a pre-set point, gradually increasing/decreasing speed as it adjusts to the change in temperature.

For more information, please visit www.lowellmfg.com or e-mail Lowell at sales@lowellmfg.com.

###

Photo file: Lowell_FDC4-2.JPG

About Lowell Manufacturing

From its headquarters located just south of St. Louis, Missouri, Lowell engineers and manufactures rack, power and audio products for the professional AV, custom installation and broadcast markets. Company history dates back to 1947 when founder Ben Lowell pioneered the idea of using a loudspeaker ceiling baffle to balance sound distribution throughout large spaces. Today, the next generation of the Lowell family works with a highly experienced sales and engineering team to convey that same spirit of innovation in developing high-performance, value-based products for the sound and communications industry.

Lowell contact info:

Kathleen C. Lane

Marketing Communications Manager

klane@lowellmfg.com

Tel: (800) 325-9660

Lowell Manufacturing Company is exhibiting at booth C9723 at InfoComm 2012 in Las Vegas, Nevada.