Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

Audio-Technica Offers New UniPoint® U843R Three-Element Multidirectional Boundary Microphone

InfoComm, Orlando, FL, June 12, 2019 — Audio-Technica (booth 5968) announces the new UniPoint® U843R Three-Element Multidirectional Boundary Microphone. With three cardioid condenser elements in a single housing, the phantom-powered U843R offers a remarkably versatile tool for surface-mount installations. It is ideal for a variety of video and audio conferencing applications, especially when used with an Audio-Technica automatic SmartMixer®. Levers on the microphone base allow easy reorientation of two elements to offer 360° or 300° coverage. Since elements can be powered and used individually or in any combination, further flexibility is easily achieved. For example, with two elements powered, the microphone can provide a figure-of-eight polar pattern; with a single element powered, the microphone functions as a standard cardioid boundary microphone. Installation and repositioning are extremely quick, thanks to four recessed pathways on the base of the microphone that enable the user to route the cable as required to accommodate any installation requirements; no tools or disassembly are needed. The microphone also offers Audio-Technica’s innovative UniGuard® RFI-shielding technology.

U843R specifications:

- Element: Fixed-charge back plate, permanently polarized condenser

- Polar Pattern: Cardioid x3

- Frequency Response: 75-15,000 Hz

- Low Frequency Roll-Off: 80 Hz, 18 dB/octave

- Open Circuit Sensitivity: -37 dB (14.1 mV) re 1V at 1 Pa

- Impedance: 100 ohms

- Maximum Input Sound Level: 134 dB SPL, 1 kHz at 1% T.H.D.

- Dynamic Range (typical): 105 dB, 1 kHz at Max SPL

- Signal-To-Noise Ratio: 65 dB, 1 kHz at 1 Pa

- Phantom Power Requirements: 11-52V DC, 2 mA typical

- Weight: 160 g (5.6 oz)

- Dimensions: 85 mm (3.35") diameter, 20 mm (0.79") height

- Output Connector: Unterminated – stripped and tinned

- Cable: 7.6 m (24.93") long unterminated-type (permanently attached to microphone), 3.8 mm (0.15") diameter, 7-conductor shielded cable; unterminated

- Accessories Furnished: Soft protective pouch

For more information, please visit www.audio-technica.com.

…ends 288 words

Photo file 1: U843R.JPG

Photo caption 1: Audio-Technica UniPoint® U843R Three-Element Multidirectional Boundary Microphone.

Click here for U843R product profile with downloadable high-res photos.

# See more here:

# Audio-Technica Promotional Video: “Always Listening to the Music That Moves Us”

# Audio for Video Techniques Videos

# Recording Techniques Videos

# Drum Miking Techniques Videos

# Additional News Releases

Celebrating over 50 years of audio excellence worldwide, Audio-Technica is a leading innovator in transducer technology, renowned for the design and manufacture of microphones, wireless microphones, headphones, mixers, and electronics for the audio industry.

—For more information on the complete range of Audio-Technica products, contact Jamie Bobek, Audio-Technica U.S., Inc., 1221 Commerce Drive, Stow, OH 44224. Tel: (330) 686-2600; Fax: (330) 688-3752; Web: www.audio-technica.com

— For further information regarding product availability and pricing in Europe, contact Rebecca Ward (rward@audio-technica.eu).