Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

Audio-Technica Displays Third-Generation 5000 Series Wireless System

The NAMM Show, Anaheim, CA, January 16, 2020 — Audio-Technica (booth 15308) is displaying its third-generation 5000 Series Frequency-agile True Diversity UHF Wireless System. Designed for use on professional tours, in stadiums, concert halls, festivals, houses of worship and other demanding audio environments, the Audio-Technica 5000 Series provides incredible audio quality and proven, critically acclaimed performance for artists, broadcasters and presenters worldwide.

The third-generation, dual-receiver 5000 Series continues to offer the highest-quality wireless live sound, with dual-compander circuitry that processes high and low frequencies separately and True Diversity operation. But now the receiver features a tuning bandwidth of 144 MHz: DF1 470–608 MHz and 657–663 MHz (duplex gap). And you have the option of selecting a standard receiver (ATW-R5220) with two balanced XLR outputs or a receiver (ATW-R5220DAN) that also includes a Dante output. Also new is an antenna cascade output that connects up to eight receivers so a single pair of antennas can feed up to 16 channels of wireless, an auto squelch feature that automatically adjusts the squelch setting to maximize operating range while minimizing potential interference, and a backup frequency that can be quickly swapped by pressing the transmitter’s multifunction button in the event of unexpected interference. A-T’s Wireless Manager software enables remote monitoring and control of the wireless system.

Two transmitters are available for use with the 5000 Series: ATW-T5201 body-pack transmitter and ATW-T5202 handheld transmitter. Both transmitters feature rugged, ergonomic metal bodies, highly visible OLED screens (switchable between standard and performance views to highlight key metering), programmable features, soft-touch controls, and switchable RF power (2 mW/10 mW/50 mW). They are available in two different frequency ranges – DE1 (470–590 MHz) and EF2 (580–608 MHz, 657–663 MHz) – to provide complete coverage of the receiver’s bandwidth. The compact ATW-T5201 is equipped with Audio-Technica’s new rugged cH-style screw-down 4-pin connector for secure connection to A-T’s cH-style lavalier and headworn microphones, or cables. The ATW-T5202 includes a high-pass filter and an industry-standard thread mount that allows for the use of six interchangeable A-T microphone capsules, as well as other compatible capsules. 5000 Series components and compatible accessories are offered as individual, à la carte products to give users the greatest possible flexibility in constructing a system that fits their needs.

A-T’s Wireless Manager software is available for download from Audio-Technica’s website.

For more information, please visit www.audio-technica.com.

…ends 383 words

Photo file: 5000series_grp.JPG

Photo caption: Audio-Technica 5000 Series wireless microphone system

# See more here:

# Audio-Technica Promotional Video: “Always Listening to the Music That Moves Us”

# Audio for Video Techniques Videos

# Recording Techniques Videos

# Drum Miking Techniques Videos

# Additional News Releases

Celebrating over 50 years of audio excellence worldwide, Audio-Technica is a leading innovator in transducer technology, renowned for the design and manufacture of microphones, wireless microphones, headphones, mixers, and turntables for the audio industry.

—For more information on the complete range of Audio-Technica products, contact Jamie Bobek, Audio-Technica U.S., Inc., 1221 Commerce Drive, Stow, OH 44224. Tel: (330) 686-2600; Fax: (330) 688-3752; Web: www.audio-technica.com

— For further information regarding product availability and pricing in Europe, contact Rebecca Ward (rward@audio-technica.eu).

Audio-Technica is exhibiting at booth 15308 at the 2020 NAMM Show in Anaheim, California.