Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

Audio-Technica Releases New Low-Profile ATW-A410P UHF Powered Wideband Antenna for Wall and Ceiling Mounting

Stow, OH, August 22, 2019 — Audio-Technica announces the ATW-A410P UHF Powered Wideband Antenna, a low-profile UHF (470-990 MHz) antenna that mounts to a wall or ceiling. It features a 4-position switchable amplifier (-10 dB/0 dB/+6 dB/+12 dB) to compensate for cable loss, along with an LED indicator to display the current gain setting. To accommodate various installation environments, the antenna’s BNC cable can be configured to exit from the top, side or rear of the antenna. Mounting bracket and screws are included.

Specifications:

- Frequency range: 470 to 990 MHz

- Connector: BNC-J

- Impedance: 50 ohms

- Power requirement: +12V DC, 60 mA or less

- OIP3: >30 dBm typical (within specified bandwidth)

- Gain: -10 dB/0 dB/+6 dB/+12 dB

- Operating temperature range: -10° C to 50° C (14° F to 122° F)

- Dimensions: 175 mm (6.9") W × 175 mm (6.9") D × 50 mm (2.0") H (without bracket)

- Weight: 390 g (13.8 oz) (without bracket)

- Accessories: Mounting bracket, screws

The Audio-Technica ATW-A410P UHF Powered Wideband Antenna is now available with U.S. MAP pricing of $349.

For more information, please visit www.audio-technica.com.

…ends 202 words

Photo file 1: ATW_AA410p.JPG

Photo caption 1: Audio-Technica ATW-A410P UHF Powered Wideband Antenna

# See more here:

# Audio-Technica Promotional Video: “Always Listening to the Music That Moves Us”

# Audio for Video Techniques Videos

# Recording Techniques Videos

# Drum Miking Techniques Videos

# Additional News Releases

Celebrating over 50 years of audio excellence worldwide, Audio-Technica is a leading innovator in transducer technology, renowned for the design and manufacture of microphones, wireless microphones, headphones, mixers, and turntables for the audio industry.

—For more information on the complete range of Audio-Technica products, contact Jamie Bobek, Audio-Technica U.S., Inc., 1221 Commerce Drive, Stow, OH 44224. Tel: (330) 686-2600; Fax: (330) 688-3752; Web: www.audio-technica.com

— For further information regarding product availability and pricing in Europe, contact Rebecca Ward (rward@audio-technica.eu).