# PRESS RELEASE

Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

FOR IMMEDIATE RELEASE

GENELEC EXHIBITS

THREE-WAY ACTIVE SPEAKERS

CEDIA EXPO, DENVER, CO, September 6, 2007 — Genelec Inc., offers home theater and custom installers its extensive range of three-way active speakers which are designed to provide a high impact listening experience for the larger home theater/multi-media room or any surround sound environment. All models employ Genelec’s proprietary Directivity Control Waveguide Technology™ (DCW™) which provides excellent stereo imaging and frequency balance even in difficult acoustic environments. In addition, all models are magnetically shielded, feature lower noise electronics, have a Signal Sensing Auto-On/Off Circuit, new crossover electronics and 12V/contact closure strip for interface to AMX, Crestron or other home automation systems. The amp panels include a dipswitch pack that allows the installer to turn the LED indicator on or off. If ON is selected, there is another dipswitch that enables all LED functions to show standby (yellow) and overload (red), or only standby. All models are available in Genelec’s matte Black finish.

The HT312A is a three-way active speaker with a 12" woofer, 5" midrange (loaded with Genelec’s DCW), and a 1" metal dome tweeter. It features an integrated electronic crossover and amplifiers (180 Watt, 120 Watt and 120 Watt), has a frequency response of 37 Hz to

21 kHz, a maximum SPL of 123 dB and measures 26 3/4" H x 15 3/4" W x 15" D.

The HT315A is a three-way active speaker with a 15" woofer, 5" midrange (loaded with Genelec’s DCW), and a 1" metal dome tweeter. It features an integrated electronic crossover and amplifiers (400 Watt, 120 Watt and 120 Watt), has a frequency response of 35 Hz to

20 kHz, a maximum SPL of 124 dB and measures 31 7/8" H x 18 7/8" W x 16 9/16" D.

The HT320AC is a dedicated center channel, three-way active speaker with dual 10" woofers, a 5" midrange and a 1" metal dome tweeter. Both the 5" midrange and 1" tweeter are mounted in a DCW for optimized directivity control. The HT320AC features an integrated electronic crossover and amplifiers (2 x 200 Watt, 120 Watt and 120 Watt), has a frequency response of 35 Hz to 20 kHz, a maximum SPL of 124 dB and measures 13 3/4" H x 37 3/8" W x 17 7/8 D".

The HT324A is a three-way active speaker with dual 12" woofers, 5" midrange and a 1" metal dome tweeter. Both the 5" midrange and 1" tweeter are mounted in a DCW for optimized directivity control. The HT324A features an integrated electronic crossover and amplifiers

(2 x 400 Watt, 350 Watt and 120 Watt), has a frequency response of 33 Hz to 20 kHz, a maximum SPL in excess of 125 dB and measures 27 9/16" H x 35" W x 15 1/16" D.

The HT324AC is the largest dedicated center channel speaker in the Genelec Custom Installation line. It is a three-way active speaker with dual 12" woofers, a 5" midrange and a 1" metal dome tweeter. Like the HT324A, the HT324AC’s 5" midrange and 1" tweeter are also mounted in a DCW for optimized directivity control. The speaker features an integrated electronic crossover and amplifiers (2 x 400 Watt, 350 Watt and 120 Watt), has a frequency response of 33 Hz to 20 kHz, a maximum SPL of 125 dB and measures 19 1/4" H x 47 5/8" W x 16 1/4 D".

The HT330A is a very powerful loudspeaker system, designed for large home theaters. It is a three-way active speaker with dual 15" woofers, a 5" midrange and a 1" metal dome tweeter. Both the 5" midrange and 1" tweeter are mounted in a DCW for optimized directivity control.

The HT330A features an integrated electronic crossover and amplifiers (2 x 400 Watt, 350 Watt and 120 Watt), has a frequency response of 31 Hz to 20 kHz, a maximum SPL in excess of 126 dB and measures 32 5/16" H x 41 1/3" W x 21 5/8" D.

Photo Files: HT324A.JPG, HT_3_Way_Group.JPG

...ends 648 words

Genelec, the pioneer in Active Monitoring technology, is celebrating over 25 years of designing and manufacturing active loudspeakers for true and accurate sound reproduction. Genelec is credited with promoting the concept of active transducer technology, which many manufacturers are just now incorporating into their products. Since its inception in 1978, Genelec has concentrated its efforts and resources into creating active monitors with unparalleled sonic integrity. The result is an active Custom Installation speaker system that has earned global acclaim for its accurate imaging, extremely high acoustic output from small enclosures, true high-fidelity with low distortion, and deep, rich bass.

Other brand and product names may be trademarks of the respective companies with which they are associated.

—For more information on the complete range of Genelec Custom Installation Systems, please contact: Genelec Inc., 7 Tech Circle, Natick, MA 01760. Tel: (508) 652-0900;

Fax: (508) 652-0909; Web: www.genelecusa.com.

Genelec is exhibiting in Sound Room 2 (SR-2) during the CEDIA Expo 2007 in Denver, CO.